Lab 2 Microscopy

I.	Purpose:	To familiarize the student with the care and use of the light microscope.

II.	Objectives:	At the end of this exercise the student should be able to:

1.	Define resolving power, field of view, depth of field (focus),working distance

2.	Name the parts of the microscope describe the function of each.

3.	Use, clean and store the microscope using the techniques describe in this lab.

4.	Calculate the resolving power of a specific lens system if the numerical 						aperture and wavelength of light is given.

5.	Calculate the total magnification of a lens system if the power of the ocular and 					objective lens is given.

6.	Make a simple wet mount of a specimen.

7.	Know how to use all the lenses including the oil immersion lens.

8.	Answer the questions at the end of the lab exercise.

III.	Introduction

Only objects 0.1mm and larger can be visualized by the human eye.  Because most microorganisms are 	much smaller than 0.1mm, a microscope must be utilized in order to directly observe them.  In general, 	the diameter of microorganisms ranges from 0.2 - 2.0 microns

A light microscope, which uses light as a source of illumination, will be employed in this lab.  There 	are several types of light microscopes.  The type used in this course is a bright-field microscope, where 	the specimen appears darker against a bright background.

IV.	Basic Principles

Resolving Power- ability of a lens system to separate fine detail

Resolution- smallest resolvable distance between two objects

Where lambda (ƛ) is the wavelength light produced by the illuminator and NA is the numerical aperture of the lens.  NA is etched on the barrel of each objective lens.

Calculate resolution of 10X objective lens ______________

Calculate resolution of 40X objective lens ______________

Field of View- the circular viewing area of a lens system.

Depth of Field- the vertical distance (thickness) of the specimen that is in sharp focus.

Working distance- the distance between the objective lens and specimen when the specimen is in focus

V.	Care of the microscope  	Observe the following precautions when using the 	microscope.

1. 	These microscopes are large and heavy.  Always use both hands when carrying the microscope.  			One hand holds the arm while the other hand supports the base.  Always carry the scope in an 			upright position.  Do not bump the scope while removing it from 	the cabinet.

2. 	Several parts are loosely connected to the scope.  When the dust cover is removed or if the 			scope is at an angle, the following parts may detach from the scope:

a.	Collector lens and blue filter (resting above the lamp),

b.	Rubber eye shields (these attach to the top of the eyepieces, the viewer's eyes rest on 				these 	shields.

c.	The eyepieces, themselves, may be loose in the eyepiece tubes.  Always take care when 			removing the dust cover, and always carry the scope in an upright position.

3. Follow cleaning instructions carefully (Preparation for viewing.).

4. Do not let the electric cord dangle or become entangled.

VI.	Parts of the light microscope

1.	 Arm and base.

All other parts of the microscope are attached to the arm or base.

2. 	Mechanical stage: The platform on which the microscope slide rests and the clamping device that 	secures the slide.

3. 	Mechanical stage control knobs (x-y control knobs): These knobs, under the stage, move the stage front to back and the slide from side to side.

4. 	Lamp (illuminator).

The lamp on/off switch is located on the base.  The light intensity can be adjusted with 	this on/off 	switch.  The lamp should be adjusted to a medium level at the start of 	viewing.  The lamp or 	illuminator usually has a blue filter that  rests on the light 	housing or under the condenser.

5.  	Iris diaphragm: adjusts the amount of light reaching the specimen. It is adjusted with 	a thin, black 	lever under the stage. It has a dramatic effect on the contrast observed in 	the specimen and may need 	to be adjusted frequently.

6. 	Lens systems: There are three lens systems: the eyepieces (ocular), the objectives (four), 	and the 	condenser.

- Eyepieces (ocular): Magnification of 10X.  The eyepieces are held rather 	loosely in the 	eyepiece tubes.  Never remove the eyepieces from the eyepiece tubes.  A rubber eye shield 	should be on the top of each eyepiece. The width between the eyepieces should be moved 	until a full circle (the viewing field) is visible with both eyes simultaneously.

- Objectives: There are four objectives: 4X (red), 10X (yellow), 40X (blue), and 100X (white, 	oil immersion objective).  The objectives are attached to a 	rotating nosepiece (nose turret).

The total magnification is calculated by multiplying the ocular magnification and the magnification of the objective in use.

3)  	Condenser: The condenser is located directly beneath the stage.  It gathers and 					conducts the light to the specimen. Although it can be raised and lowered with the condenser 			adjustment knob, the condenser should remain at its highest position.

7.	 Focusing knobs: located on both sides of the microscope.

The larger, inner coarse adjustment knob moves the stage up and down much faster and farther 	than 	the smaller, outer fine adjustment knob.  The coarse adjustment knob is used ONLY with the low power 	(4X, 10X) objectives.  When focusing under the 40X or 100X objective, ONLY use the fine 	adjustment, never the coarse adjustment.

8.	Nosepiece:  Holds the objective lenses

Refer to each of the following procedures every time the microscope is used.

VI. 	Preparation for viewing

- If you have not done so, carefully remove a scope from the cabinet and set it on your lab bench.  	Remove the dust cover.  Check that no parts are loose or missing.  	Immediately contact the instructor if 	parts are missing or anything is wrong with the scope.

- There are two ways to position the oculars: toward or away from the stage.  The 	‘head’ containing the 	oculars is loosened or tightened using the silver Head Positioning 	Screw protruding below the 	microscope head. Do not loosen the screw too much as the head may detach completely.

- Plug in microscope.  Be sure the electrical cord is not dangling off of the lab bench or is 	not entangled.

4. 	Use the coarse adjustment knob to move the stage to its lowest level.

5.  	Cleaning the microscope.  Clean all objective lenses with lens paper  and, if necessary, liquid lens 	cleaner.  Place a small amount of liquid lens cleaner on the swab.  Use a 	fair amount of pressure to 	clean the lens.  Dry the lens with a different swab.  Use different swabs for each lens.  Do not use 	liquid lens cleaner on the eyepieces.  Dust on the eyepieces, or elsewhere, may be removed using the 	blower brush.  NEVER remove any parts.

6.  	Before use, clean all slides, top and bottom, with Kimwipes.  Place a coverslip over the 	specimen on 	the slide.  Do not use a coverslip if viewing prepared slides.

7.  	Adjust the condenser to its highest level.  Turn on the lamp.  Adjust the on/off switch to 	a low/medium 	light level.

8. 	Rotate the nosepiece until the 4X objective clicks into place.

9.  	Place the slide on the stage so that it is held within the slide holder clamping device.  The slide must 	lie flat on the stage. Using the mechanical stage knobs, position the slide 	so that the specimen is in the 	exact center of the light coming through the condenser.

10.  	While looking through the eyepieces, adjust the width between the eyepieces until a 	single, circular 	field is seen simultaneously with both eyes.

11. 	If problems are encountered during viewing, repeat the procedure.  If problems persist, 	review the 	Common Problems section at the end of this document.

VIII. 	Viewing the specimen under the 4X, 10X, and 40X objectives

- Always start with a low power objective (4X or 10X) clicked into place.

The lowest power objectives have the largest field of view (a larger portion of the slide 	can be seen), 	making it easier to initially find the specimen.

2.  	Move the stage to its lowest point with the coarse adjustment knob.  In other words, the 	stage should 	be as far away from the objective as possible.

3.  	Light control

Light intensity is a essential aspect of microscopy.  For optimal viewing, the light must be adjusted at 	each magnification.  Perform the following steps to adjust the light.  Always adjust the light while 	looking through the eyepieces.

a.  	Adjust the light intensity switch that turns the lamp on.  Begin at a low/medium 		level.

b. 	The entire viewing area (field) must be filled with light.

c.  	Locate the thin, black iris diaphragm lever under the stage.  Adjust this lever to 	a medium/low 	light level.  The iris diaphragm will need to be adjusted as 	magnifications increase.

4. 	Under low power, SLOWLY focus with the coarse adjustment knob until the specimen 	comes into 	view.  Adjust the light as instructed as needed.

Many specimens are very small and may look like specks at this magnification.  If the stage moves 	too quickly, you may go past the specimen without seeing it.

5.	 Refine the image with the fine adjustment knob and by adjusting the light.

- Important!  Before switching to the next objective, move the slide so that the desired specimen is 	located in the center of the field (circular viewing area).

7. 	SIGNIFICANT POINTS WHEN FOCUSING UNDER THE 4X,10X, AND 40X 	OBJECTIVES!

- Always start with a low power objective (4X or 10X).  After making appropriate 	observations, 	rotate the nosepiece until the next objective clicks into place.  Do 	not skip objectives.

- Do not move the stage up or down before rotating the nosepiece to the next objective. When properly focused, there is no need to adjust the objective's distance from the stage before increasing the magnification.

- DO NOT USE THE COARSE ADJUSTMENT KNOB WHEN FOCUSING 	UNDER THE 	40X OBJECTIVE! ONLY USE THE FINE 	ADJUSTMENT KNOB!

- Before increasing the magnification, always move the slide so that the desired 	specimen is 	located in the center of the field.

e.   	Remember to adjust the light each time the magnification is changed if the area 					observed is too dark.

IX. 	100X Oil Immersion Procedure (will not be used in this exercise)

Immersion oil is used with the 100X objective because it increases the resolution.  The oil should come 	in contact with both the lens of the 100X objective and the slide or coverslip.  This prevents the 	scattering of light rays.

1. 	Position the specimen i in the EXACT CENTER of the viewing field under the 40X objective.

- NOTE!  Again, do not move the stage up or down before rotating the nosepiece to the 100X 	objective. Rotate the 40X objective away from the slide but do not yet click the  100X objective into 	place.

3.  	Put a small drop of immersion oil on the slide/coverslip directly over the light.

4. 	 Rotate the nosepiece until the 100X oil immersion objective is clicked into place.

5.  	DO NOT USE THE COARSE ADJUSTMENT KNOB WHEN FOCUSING 	UNDER THE 100X 	OBJECTIVE! ONLY USE THE FINE ADJUSTMENT 	KNOB!

6.  	Adjust the light for optimal viewing.

7. 	 In order to determine the size of your specimen, you will need to estimate utilizing the size of the 	field (circular viewing area).  When you observe your specimen, estimate 	its size by comparing it with 	the size of the field. Place a clear plastic ruler with mm markings on top of the stage of your microscope. 	Focus the microscope with the lowest power (4X) objective lens.  Count how many divisions (mm) of 	the ruler fit across the diameter of the field of view.

Objective			Size of field of view

4X						mm

10X						mm

40X						mm

When finished viewing, complete the Student Microscope Checklist.

X. Common Problems

1. 	The field is dark.

Is the light on?

Is the objective securely clicked into place?

Is the diaphragm open?

Is the slide lying flat on the stage?

2. 	You are not sure if you are looking at dirt on the objective lens or the specimen.

Use the mechanical stage knobs to move the slide slightly while looking through the eyepieces.  If what 	you are looking at does not move, it is probably dust or dirt on the 	objective.  If it does move, it is on 	the slide.

Rotate the ocular gently between your fingers.  If what you are looking at rotates, it is probably dirt on 	the ocular.

3. 	You cannot find the specimen.

The stage may be too far from the objective.  Did you start with the stage as close as possible to the low 	power objective?

Is the specimen directly over the light?

Is the slide secure and flat in the mechanical stage?

Did you start with a low power objective and focus on the lower objectives first?

Have you adjusted the light?

Are you moving the adjustment knobs too quickly?  Work slowly so you do not miss the specimen.

4. 	You are having trouble focusing.

Always start on a low power objective, and focus here first.

Focus SLOWLY!  It is very easy to move past the specimen if the adjustment knobs are 	moved too 	quickly.

Be sure to look in the ocular while you are focusing with the adjustment knobs or 	changing the light 	intensity.

Adjust the light.

Press down on the stage with your fingertips.  Does the stage move?  If so, tighten using 	the knob next 	to the coarse adjustment.

5. 	You lose the specimen when switching from the 40X objective to the oil immersion 	objective.

Was the specimen in the exact center of the field before switching to the 100X objective?

Is the 100X objective lens clean?

Have you adjusted the light?

Have you refined the image with the fine adjustment?

XI 	Assignment (see attached Lab Report):

A.	Preparation of a Wet Mount

1.	Add one or two drops of IKI (Lugol’s) solution to the central region of a clean glass slide.

2.	Using a toothpick gently scrape the inside of your cheek to obtain epithelial cells.

3.	Place the cheek cells into the IKI (Lugol’s) on the slide and mix.

4.	Place the cover glass so that one edge touches and glass slide and then gently lower the cover 			slip.

5.	View the specimen with all objective lenses except the oil immersion lens. Draw what you see 			the data sheet provided.

B.	Preparation of Hair

1.	Prepare a wet mount of two crossed hairs

2.	Study the slide under 40X, 100X, and 400X (total magnification)

3. 	 Observe the differences in depth of field, field of view and working distance 					between these powers.

C.	Letter "e".

1.	Prepare a wet mount using the letter "e" as the specimen.  Place the preparation with the letter 			"e" on stage so that you can read the letter "e" as in the previous sentence.

2.	Study the slide under 40X, 100X, and 400X (total magnification).  What observation did you 			make when you looked at the "e" for the first time under low power (40X)?

______________________________________________________________

3.	Using 40X total magnification (low power) while looking at the letter"e", move 		the 			stage forward and backward and right  then left.  What happens to the "e".

______________________________________________________________

D.	Human Blood smear (if time permits).

1.	Obtain a prepared slide of human blood and observe under 40X, 100X and 		400X.

What cells did you find?

______________________________________________________________________

Lab Report

# Microscopy

1. 	Draw and label the letter "e" after focusing with 10X and 40X objectives.

2. 	Draw and label the crossed hairs after focusing with 10X and 40X objectives.

3. 	Draw and label the cheek cells (squamous cells) after focusing with 10X and 40X 	objectives.

4.	If you had enough time to look at a prepared Human Blood Smear, what cells did you identify?

_________________________________________________________________________

5. 	Define resolution.

6.	 What is the total magnification of the following?

Ocular magnification		Objective magnification			Total magnification

10X				40X

10X				100X

7. 	What is the function of the iris diaphragm?

8. 	List two instances when the coarse adjustment knob is never used.

9.	 When should the lenses be cleaned?  What is the correct way to clean them?

10. 	Why is immersion oil used with the 100X objective?

_________________________________________________________________________

11. 	List two common problems associated with using the microscope and how you would go 			about solving it.

12.	Using the following formula below calculate the resolving power of your oil immersion 	lens.

________________________________________________________________

Student Microscope Checklist

When finished using the microscope, complete the following.

Check off each step when completed.

Name:							Lab Section:

Date:				Microscope Number:

Bring the stage to its lowest level.

Click the 4X objective into place.

Remove the slide and dispose of appropriately.  Wipe prepared slides until ALL oil/dirt is removed (top and bottom).

Clean objective lenses with lens paper, and, if using oil, use lens cleaner.

Clean eyepieces with lens paper.

Clean condenser lens with lens paper.

If necessary, clean the stage with a damp Kimwipe.

Turn the light switch OFF.

Follow teacher's directions for method to secure the electrical cord.

Replace the dust cover if one is available.

Return the microscope to the appropriate location in the cabinet.