Electric Field Line Mapping      Part I

Materials:

- Extech DC Regulated Power Supply

- Overbeck Electric Field Apparatus (Central Scientific), with Templates #1 & #2, Plates: “Two small circular conductors”, “Faraday Ice Pail”, “Parallel Plates”, & Ruler marked in mm.

- Multimeter with (2+ each) Black & Red Banana Cords

Objectives:

- Learn how to make measurements of electric potential

- Learn how to map regions of equal electric potential

- Learn how to map and calculate the electric field using equal potential lines

- Learn how to infer the distribution of charge on conductors

Background Information

- The strength of the electric field near a conductor is proportional to the charge density on the conductor

- Conductors in electrostatic equilibrium are equal potential surfaces

- Electric field lines are everywhere perpendicular to lines of equal potential

- Equal potential lines indicate paths in which the electric potential has no change

- Electric field lines indicate paths in which the electric potential changes the maximum amount per unit distance

- Lines of equal potential never intersect one another

- Electric field lines never intersect one another

- The size of the electric field is given by V/x, where x is measured along the direction of the field line

- The direction of the electric field is toward smaller values of electric potential

General Procedural Information

- Connect conductor plates on bottom of Overbeck device

- Disconnect wires when changing conductor plates

- Hook template on hooks and trace correct conductors onto paper

- Mark potential points in pencil

- Adjust DC Power Supply to 6.0V

- Connect the left plate to the black power supply outlet and the right plate to the red power supply outlet.

- Write 0V by the plate connected to the black power supply outlet

- Write 6.0V by the plate connected to the red power supply outlet

- Use 200V ---- setting on the multimeter

- Connect the common outlet of the multimeter to the 0V plate, connect the red outlet of the multimeter to the measurement arm

Two Circular Conductor Procedure

- Take 5 data points each for 1.0V, 2.0V, 3.0V, 4.0V, and 5.0V.

Point & Plane Conductor Procedure

- Take 5 data points each for 1.0V, 2.0V, 3.0V, 4.0V, and 5.0V.

Parallel Plate Procedure

- Take 6 data points each at 1.0V, 3.0V, and 5.0V, mapping into regions outside the area between the plates.

Electric Field Line Mapping      Part II

General Report Instructions

- Work in Pencil

- Turn in one set of data and calculations per group

- Each group member should keep complete notes of the lab work

- Write the voltage for each different value on your paper

- Draw smooth lines through each equal potential data set

- Use |V/x| to calculate the size of the electric field

- Write “a”, “b”, “c” on each data page using the appropriate diagram below.

- Calculate the size of the electric field at points “a”, “b”, “c” directly on your data paper.

- Show and label your equation, calculation, answer, and units directly on the data paper.