Name______________________		Date_____________

PHYS 1402 General Physics II

Resistors in Series and Parallel

Equipment

Circuit Board w/ 3 Resistors

2 Multimeters

Battery Eliminator (6V)

Connection Wires

# Objective

The objective of this experiment is the study of the behavior of series and parallel resistive circuits. The student will measure the equivalent resistance of resistors connected in series and parallel. Also, the student will measure currents through and potential differences across resistors connected in series and parallel. The measurements will be compared with theoretical predictions.

# Theory

## A.	Series Circuit

A series circuit is one in which the elements (resistors and voltage source) are arranged to provide a single conducting path for current as in Figure 1.

In series circuits:

1.	The current is the same at any point in the circuit since there is only a single path for

moving charges.

IT = I1 = I2 = I3    		Formula 1 - series

where IT is the current through the entire circuit and I1, I2, etc. represent the current

through each individual resistor.

2.	From the Law of Conservation of Energy, the sum of the voltages across the resistors

should equal the voltage of the source.

VT = V1 + V2 + V3 + ...		 Formula 2 – series

where VT is the voltage applied to the circuit, and V1, V2 etc. are the potential drops

(“voltage drops”) across the separate resistors

- The total resistance of the circuit should equal the sum of the separate resistances.

RT = R1 + R2 + R3 + ...	Formula 3 – series

## B.  	Parallel Circuit

A parallel circuit is one in which two or more elements (resistors and voltage source) are connected across two common points in the circuit providing separate conducting paths for current as in figure 2.

In Parallel Circuits:

1.	The voltage is the same across each resistor, and is equal to the voltage of the source.

VT = V1 = V2 = V3  = …	Formula 1 - parallel

where VT is the voltage applied to the circuit, and V1, V2, etc. are the potential drops (“voltage drops”) across the separate resistors.

2.	The current in a given path will vary inversely with the resistance (small current for

big resistance, and big current for small resistance).  From the Law of Conservation

of Charge, the sum of the separate currents through each resistor will equal the total

current from the source.

IT = I1 + I2 + I3 + ...		Formula 2 - parallel

where IT is the current through the entire circuit and I1, I2, etc. represent the current

through each individual resistor.

3.	The total resistance of a parallel circuit is less than the resistance in any one branch

of the circuit.

Formula 3 – parallel

where RT is the total resistance in the circuit, and R1, R2 etc. are the resistances of each of the separate resistors.

# Experimental Procedure

Procedure (1):

NOTE: in this procedure, the resistor should NOT be connected to the battery.

1.	Using the ohmmeter, measure the resistance of each of the resistors and record the

values below.

R1 = _________ Ω             R2 = _________ Ω          R3 = _________ Ω

2. 	Connect R1, R2 and R3 in series and measure their equivalent resistance and record in

Table (1).  Show sample calculations to the right of the table.

3.    Connect R1, R2 and R3 in parallel and measure their equivalent resistance and record

in Table (2).  Show sample calculations to the right of the table.

|  | Equivalent Resistance for R1, R2 and R3 in series Ω |
| --- | --- |
| R equivalent Measured |  |
| R equivalent Calculated |  |
| % difference |  |

Table (1):  Series Connection                   Sample calculations

|  | Equivalent Resistance for R1, R2 and R3 in parallel Ω |
| --- | --- |
| R equivalent Measured |  |
| R equivalent Calculated |  |
| % difference |  |

Table (2):  Parallel Connection                Sample calculations

Procedure (2): Series Connection

1. 	Connect R1, R2 and R3 in series to the battery eliminator set at 6-volts as shown in Figure (1).

2.	Using a voltmeter, measure the potential difference across each of the resistors and

the battery and record in Table (3). Again, do NOT forget the units.

3.    Insert the ammeter at the appropriate points in the series circuit and measure the

current passing through each of these points and record in Table (3).

Figure 1

Procedure (3): Parallel Connection

1.	 Connect R1, R2 and R3 in parallel to a 6-volt battery as shown in Figure(2).

2.	 Using a voltmeter, measure the potential difference across each of the resistors and

the battery and record in Table (4).

3.	 Insert the ammeter at the appropriate points in the parallel circuit and measure the current passing through each of the resistors and the current  provided by the battery and record the values in Table(4).

Figure 2

# Data

Table (3):  Series Connection

| Potential Difference | Electric Current | Resistance |
| --- | --- | --- |
| VR1 = | IR1 = | R1 = VR1 /IR1 = |
| VR2 = | IR2 = | R2 = VR2 /IR2 = |
| VR3 = | IR3 = | R3 = VR3 /IR3 = |
| Vbatt = | Ibatt = | Req = Vbatt /Ibatt = |
| VR1 + VR2 + VR3 = |  |  |

Table (4):  Parallel Connection

| Potential Difference | Electric Current | Resistance |
| --- | --- | --- |
| VR1 = | IR1 = | R1 = VR1 /IR1 = |
| VR2 = | IR2 = | R2 = VR2 /IR2 = |
| VR3 = | IR3 = | R3 = VR3 /IR3 = |
| Vbatt = | Ibatt = | Req = Vbatt /Ibatt = |
|  | IR1 + IR2 + IR3 = |  |

# Analysis

1. 	In the series circuit, compare the battery potential difference Vbatt to the sum

VR1 + VR2 + VR3 by calculating the percent difference

Are the two quantities within 5 % of each other? = __________

2.	 In the series circuit, compare the currents through the resistors. Are they within 5%

of each other? _____________

3.	 In the parallel circuit, compare the potential difference across each of the resistors

and the battery. Are they within 5% of each other? ___________

4. 	 In the parallel circuit, compare Ibatt, the total current provided by the battery, to the

sum of the currents through the three resistors IR1 + IR2 + IR3 by calculating the

percent difference.

Are the two quantities within 5 % of each other? ___________

5. 	Using the data collected in procedures (2) and (3), apply Ohm's law to calculate the

values of the resistances and the equivalent in each of the series and parallel circuits

and enter your results in Tables(3) and (4) respectively.

Are the values for equivalent resistances in tables (3) and (4) within 5 % of the

respective measured equivalent resistances found in tables (1) and (2) ? ________

# Hand In

Hand in this handout with the completed data tables and the answers to the questions.  This time, you can answer the questions directly on the lab handout instead of on a separate sheet of paper.