## Boyle’s Law

Equipment Needed

Multi-Clamp, Pasco ME-9507

Clamp, Table Black Humboldt H-8255

Mass Set, Gram w/ rack (Assorted)

Mass, 500g (2)

Mass, 1kg

Boyles Law Apparatus, Sci. Kit WW64710M00

Clamp, Tubing

Caliper, Digital General

Barometer (not in stock)

Figure 1

# Theory

Robert Boyle discovered a relation between the absolute pressure Pabsolute and volume V of a gas. This relation is known as Boyle's Law. At constant temperature, the volume occupied by a given mass of gas is inversely proportional to its absolute pressure.

Equation 1

where

“k” is the constant of proportionality for gas at a given temperature.

The gauge pressure of a confined gas can be changed by using the cylinder and piston assembly as shown in Figure 1. The gauge pressure Pgauge is proportional to the total force F applied to the piston divided by its area A:

Equation 2

The current value of atmospheric pressure Patmosphere is added to the gauge pressure to give the absolute pressure Pabsolute required to satisfy Boyle's Law.

Equation 3

Plotting Absolute Pressure vs. Volume will result in a curve called a hyperbola.

Plotting Absolute Pressure vs. 1/Volume will result in a straight line.

#### Procedure

- Mount the syringe in the cylinder holder as shown in Figure 1.  The clamping arrangement is for stability.  Do not tighten the 3-prong clamp too tight as it can deform the cylinder thus impeding the plunger.

- Adjust the piston about ¼ down the cylinder by releasing air from the rubber tip.  The graduations on the cylinder indicate the actual volume in cm3 at the position of the piston.

- Add masses to the platform equaling 500g, 1000g, 1500g, 2000g, 2400g. Record the volume each time mass is added.

- Complete Data Table 1 with the measurements of force, area, pressure, volume and 1/volume. The applied force is:

where

M is mass on the piston and

- Plot Pressure versus Volume and Pressure versus 1/Volume as illustrated in Figure 2—3.

Figure 2—3

DATA TABLE 1

# Patmosphere (barometer): ___________   Pa

| To go from | Multiply by | To get |
| --- | --- | --- |
| kPa | 7.5006 | mm of Hg |
| mm of Hg | 0.13332 | kPa |

Diameter of Inner Barrel:__________ m	Area of Inner Barrel:   (D2/ 4: __________m2

| Added Mass, M | Force M*9.79 m/s2 | Area (from above) | Gauge Pressure (Force / Area) | Absolute Pressure: (gauge pressure + atmospheric pressure) | Volume | 1/Volume |
| --- | --- | --- | --- | --- | --- | --- |
| (kg) | (N) | (m2) | (Pa) | (Pa) | (cm3) | (cm-3) |
| 0.5 |  |  |  |  |  |  |
| 1.0 |  |  |  |  |  |  |
| 1.5 |  |  |  |  |  |  |
| 2.0 |  |  |  |  |  |  |
| 2.4 |  |  |  |  |  |  |

Do you get a curve when you plot Pressure vs. Volume?

Do you get a straight line when you plot Pressure vs. 1/Volume?