Rotational Collisions

Equipment Needed

Dell Laptop Computer

AC Adapter, Dell Laptop

Ruler, 12-15in

LabQuest Mini, Vernier LQ-MINI

w/ Mini USB Cable, Vernier CB-USB-MINI

Photogate & Pulley System, Pasco ME-6838A

w/ BT Photogate Cable, Vernier PG-BTD

Rotational Motion Apparatus, Pasco ME-9341

Calipers, Digital Mitutoyo 500-474

Scale, Digital Sartorious BP-6100

Figure 1

Introduction

A rotating platter has rotational kinetic energy, RKE, and angular momentum, L.  In a collision between two platters, the sum of the angular momentums  following the collision will be equal to the sum of the angular momentums before the collision.  In this lab, you will investigate this relationship in a particular case—that in which one of the platters has no initial angular momentum.

Procedure

- Set up the apparatus as shown in Figure 1.  Mount the main platter so the step pulley is facing downward.  The pulley/photogate assembly should be mounted as shown with the rubber band so that the pulley will turn as the platter turns.

- Click File → Open

The address is:  Experiments\Probes & Sensors\Photogates\Pulley.cmbl

- Hold the auxiliary platter just above the main platter of the Rotational Motion Apparatus.  Give the main platter a spin using your hand.  Start Logger Pro.  Drop the auxiliary platter onto the spinning platter.

- Examine the graph, you should note that there are two sections that are straight lines, representing the change in velocity of the one platter and the addition of the second platter.  They are joined by a region where the platter abruptly slowed down due to the second platter colliding with it.

- Do a statistical analysis of a short period before the change and a short period after the change.

- Determine the angular velocity immediately before the collision  and immediately after .  Record these values in the data table.

- Repeat three times.

- Next drop the steel bar onto the moving platter three times and complete the same steps with it.

Analysis

Angular momentum L is equal to the moment of inertia I times the angular velocity .

Or

Calculate , the angular momentum before each collision, and , the angular momentum after each collision.

For I of the platters:

For I of the bar (the step pulley can be neglected):

(see Figure 2).

Check the conservation of momentum by calculating the percentage difference between  and  in each case.

Platter radius = __________

Bar dimensions

Figure 1

A = __________

B = __________

Data Table

| Trial | Moving Platter | Platters Together |  |  |  |  | % Difference |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 |  |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |  |