Simple Harmonic Motion

Pendulum

Equipment Needed

Dell Laptop Computer

AC Adapter, Dell Laptop

Protractor

Tape Measure, 5m Stanley 33-158

Ring Stand Table Rod, Tapered Vertical 0.75inx90cm

Cylinder Set, Specific Heat (w/ hook)

Clamp, Pendulum Arbor Sci. P1-7139

LabQuest Mini, Vernier LQ-MINI

w/ Mini USB Cable, Vernier CB-USB-MINI

Photogate, Vernier VPG-DG

w/ BT Photogate Cable, Vernier PG-BTD

Ringstand, Miniature

String, Black

### Introduction

Any motion that repeats itself in equal intervals of time is called periodic motion.

A special form of periodic motion is called Simple Harmonic Motion (SHM) where the restoring force is directly proportional to the displacement of the mass.  It can serve as a mathematical model of a variety of motions, such as the oscillation of a spring.  In addition, other phenomena can be approximated by simple harmonic motion, including the motion of a simple pendulum.

A special feature of SHM is that the period, T, of the oscillating system does not depend on the displacement, thus making the system a good time-keeping device.  The period is the time it takes the pendulum to swing to one side and back to the starting point, then to the other side and back to the starting point again.

A simple pendulum is a point-like mass (called a bob) on the end of a string. The length (l) is measured from the pivot point to the center of mass of the bob.  The period of a pendulum was used for centuries as an accurate timekeeper. It is constant if nothing else about the pendulum is changed. The variables that can be changed to study their effect on period are mass, length and angle of displacement from the vertical.

Procedure

Assemble a pendulum by attaching the top end of the string to the pendulum clamp and attaching a bob to the lower end. This lab can be done with a stopwatch or a computer.  Release the bob from approximately 15°.

Stopwatch

Time 10 cycles and enter the time (t) into the data table.

Computer

Use the pendulum timer file.

The address is: File → Open Experiments\Probes & Sensors\Photogates\Pendulum Timer.cmbl

Determine the time (t) for 10 cycles. Enter in the data table.

Measure the period for the 5 different lengths in the table, released at approximately 15°.

Data Table

| Time (t) for 10 cycles (sec) | Period T (sec) | Length l (m) | () |
| --- | --- | --- | --- |
|  |  | 0.75 |  |
|  |  | 0.7 |  |
|  |  | 0.65 |  |
|  |  | 0.60 |  |
|  |  | 0.55 |  |

The period of oscillation depends on the parameters of the system, and, for a pendulum, this is given by:

Or

Where

l is the length of the pendulum and

g is the acceleration due to gravity.

Plot a graph of . (Use MS Excel®)

Find the trend line w/ equation.  Solve for g from slope.

The slope, m, is equal to

So

Compare to the accepted (don’t confuse m for slope and m for meters)

Calculate % error:

__________________