# Vector Equilibrium

##### Equipment Needed

Mass and Hanger Set, Pasco ME-8967

Protractor

Ruler

Force Table, Pasco ME-9447B

Graphing Paper Different Types Blank

## Typical Setup

## Terminology

- gram force (gf): the weight force produced by a known amount of mass in grams. For example, 35.0 gf (gram force) = 0.0350(9.80 N (newtons). Use of gram force simplifies our work substantially for this lab.

- equilibrium: the state of an object that has no accelerations of any type. In this lab equilibrium translates to:

and

.

Overview

Two known vectors are added graphically and by the component method. You will then experimentally find the vector that is the opposite (negative) of this sum and compare the experimental to the theoretical value.

## Introduction

The equilibrium of a particle in two dimensions is established when the sum of all the forces on it add to zero in a vector sense, i.e.:

Equation 1

Equation 1 can be replaced by two simpler equations when working in two dimensions:

Equation 2 and,

Equation 3

Equation 1 is used when a graphical addition of vectors is to be done, and Equations 2 and 3 is used for algebraic calculations.  The two equation sets are equivalent in every way.

In this lab, there are only two forces to add, thus

,

where

and  are gram force vectors produced by masses hung over pulleys attached to the vector force table.

You will form the sum  by both graphical and algebraic methods, then set up these forces on the table and experimentally find the vector which cancels the effect of  and . This vector will be called ,  and satisfies

Equation 4

or equivalently that,

.	Equation 5

Procedure

In this laboratory you will add two vectors,

@ 20° Azimuth 	Equation 6

@ 155° Azimuth	Equation 7

three different and independent ways;

- Graphically (on a sheet of paper)

- Algebraically

- Physically.

### Part 1

Using a piece of paper, graphically add  and .  You will add these vectors on paper so that the majority of the page is used in this sum. You must use an appropriate scale factor in an attempt to get the largest graph possible on the page.  Using a ruler and a protractor, determine the length of the sum of  and  in gf units, and its angle  measured from the  axis.

________________

_______________

### Part 2

Now carry out the algebraic sum of  and  by calculating their x and y components from their definition in Equations 6 and 7, not from your graph. Show your work here.

_______________

_______________

_______________

_______________

_______________

_______________

Now calculate the length and angle of this vector sum:

_______________

_______________

Do these values agree with those measured from your graph in Part 1?

### Part 3

In this part you will use the experimental apparatus to calculate this vector sum. You must, however, complete all the work in Parts 1 and 2 first. Load the force table with  and  forces as given in Equations 6 and 7. Remember that the hangar’s mass is part of the gram force you are using.  Load the third hangar with the weight value for  from Part 2 in gram force (also including the hangar’s mass in this value). Place this hangar at the angle  on the force table. We will call this third weight the vector . If  has the value of  but in the opposite direction, it will cancel out  and the ring will be motionless at the center of your table without having to rest against the restraining pin. The best way to find out if it is a true state of equilibrium is to lightly tap the ring. If the ring remains centered upon tapping, and does not rest against the pin, you have experimentally found the vector  which cancels out .  Another way of saying that is that the sum of the forces acting , and that there is thus no net force acting on the ring.

Experiment with varying the mass of hangar 3 (down to the gram) and its angle until you get the best experimental state of equilibrium that you can.  Once the best experimental condition has been achieved you might most simply take all of this stuff to the electronic balance and weigh it all together at one time. Report the results of this experimentation here, remembering that this is the experimental value for vector .

_______________ gf

_______________

Part 4

The value of  from part 3 above should equal the algebraic sum of Part 2. And, if you subtract 180( from the angle from Part 3 above, this value should equal the angle you calculated in Part 2.

How well do these results compare? (remember to use correct significant figures)

What is the likely cause of the discrepancies you observe?