The Diffraction Grating

to

Measure the Wavelength of Light

# Description

In this laboratory experiment we will use a diffraction grating to measure the wavelength of a HeNe laser.

# Equipment Needed

Diffraction Grating, 100-300-600 Paton Hawksley TE 214 w/ Pasco Lens Holder

Laser, HeNe ~670nm

AC Adapter, Laser HeNe if necessary

Viewing Screen, w/ 2 Binder Clips Pasco OS-8460

Jack, Table, Silver

Meter Stick (2)

Optics Track, 120cm Pasco OS-8508

Rubber Band

# Note:  The HeNe laser is preferred because it is more stable (consistent) and more orders may be observed due to its higher wattage.

# Introduction

The diffraction grating consists of a large number of equally spaced parallel slits.  A grating can be made by cutting parallel lines on a glass plate with a precision ruling machine.  In a transmission grating, the space between any two lines is transparent to the light and hence acts as a separate slit.  A grating with 100 slits per millimeter has a slit spacing .  The gratings we will use in this lab have three windows per slide.  They are generally 100, 300, and 600 lines per millimeter.  You will need to calculate d for the 300 and 600 lines per millimeter windows.

Figure 1 demonstrates the geometry of light after it has passed through the diffraction grating.  We show just two of the slits for simplicity of illustration.

Figure 1

Figure 2 shows the geometry between the grating and the screen.  The pictured angle  as shown denotes the second maxima.  This is the same  as shown in Figure 1  (Figure 1 angle  is exaggerated for dimension lines.)  There is a  for each .

Figure 2

Figure 3 combines Figure 1 and Figure 2.

To show where the maxima are created we need to know the value of

.

This value was illustrated in Figure 1.  Since this is the difference in distance of the two light beams from the two slits to the screen we will expect a maxima to appear at this point.  Note:  The maxima occur when the difference in distances equals a multiple of the wavelength of the light.  We also know that this difference will be equal to one multiple of the wavelength between the two beams so

Equation 1

We know that

Equation 2

We can find the beam length using the identity (Pythagorean Theorem)

.			Equation 3

Then solving for h (beam length) we get

Equation 4

Also

Equation 5

Substituting Equation 4 into Equation 5 we find

Equation 6

We can now substitute Equation 6 into Equation 1 and we get

Equation 7

When the first maxima occurs we know that Equation 7 equals  where .  We can substitute this into Equation 7 and we get

Equation 8

In Equation 8 we have established measurable variables with which to calculate the wavelength of the light beam.

Safety

Although these lasers are not particularly dangerous, we should take a few simple precautions to prevent the unlikely event of eye damage.

- Never look directly into the laser beam.  Laser light has a high intensity and can also be easily focused.  A direct shot of the laser beam on your eye will be focused by your cornea onto a small spot on your retina and can burn or possibly detach the retina.

- Never hold a reflecting object by hand in front of the laser beam.  This prevents the possibility of accidentally shining the light into your eyes.

- Keep your head above the plane of the laser beam.

- Whenever the light strikes an object, there will be a reflection.  At times the reflections can be almost as strong as the incident beam.  Know where the reflections are and block them if necessary.

- The laser has a shutter in front of the beam.  When not taking data, place the shutter in front of the laser beam.

# Procedure

## Figure 4 Setup and Layout

- Set up your lab similar to Figure 4.  Figure 5 shows detail of meter stick mount.

- Line up the laser to hit the meter stick on the 50 cm point.  The distance from the laser to the screen is not critical.

- Set the grating with the 100 lines / mm window between the laser and the screen.  Note:  When handling the gratings be careful not to touch the window.

- Make geometric adjustments.

  - Vertical—where the dot measurements are easy to read on the meter stick.

  - Horizontal—scatter the dots as much as possible by increasing the value of L.  You can move the grating closer and farther from the screen.

Figure 5 Detail of meter stick mount.

- Record the distance values.

  - Once you establish the L distance set it should stay the same for all of the x’s.  Record this distance.

  - Record the distances x of the light dots from the 50 cm mark on the meter stick.

- Repeat the steps 3,4, and 5 for the 300 and 600 line/mm windows on the diffraction grating.  You may notice that the distance L must be readjusted for each window.

Data Tables

| Grating Window 100lines/mm |
| --- |
|  | L= | d= |
| n | X | Calculated |
| 1 |  |  |
| 2 |  |  |
| 3 |  |  |
| 4 |  |  |
| 5 |  |  |
| 6 |  |  |
| 7 |  |  |
| 8 |  |  |
| 9 |  |  |
| 10 |  |  |
|  | Average |  |

Note:  You will be limited in the number dots you can get with the denser gratings.  The instructor may not choose to take data from all three gratings on the card.

| Grating Window 300lines/mm |
| --- |
|  | L= | d= |
| n | X | Calculated |
| 1 |  |  |
| 2 |  |  |
| 3 |  |  |
| 4 |  |  |
| 5 |  |  |
|  | Average |  |

| Grating Window 600lines/mm |
| --- |
|  | L= | d= |
| n | X | Calculated |
| 1 |  |  |
| 2 |  |  |
| 3 |  |  |
| 4 |  |  |
| 5 |  |  |
|  | Average |  |

Graph

Rewrite Equation 8

Equation 9

Create a graph for each of the diffraction gratings.

Use a trend line and find the slope of the curves.

Using the slope, find the % error.