Name_______________________

# Torques

## Equipment Needed

Fulcrum Kit   D4-L

Hanger clip   D4-L

Pivot clip   D4-L

Jack, Table   G2-L

Mass Hanger, 50 g (3)   H2-L

Mass Set, Gram   H2-L

Meterstick   H4.5-L   in window

Lab setup

Fig 1A

Fig 1B   alternative setup

Fig 2   note:  the pivot clip tightening screw needs to be down as shown; otherwise, balance will be difficult to achieve.

## Theory

For a body to be in static equilibrium, two conditions have to be met:

and

where

F is force

( is torque.  (The torque is the force times the lever arm, r)

The first condition, , is concerned with translational equilibrium and ensures that the object is not moving linearly or is moving at a uniform linear velocity.

The second condition, , is concerned with rotational equilibrium and ensures that the object is not rotating or rotating at a uniform angular velocity.

## Procedure  (For each setup, draw a scale diagram of the setup)

- Measure the mass of a meterstick and then place the meterstick on a support stand.  Adjust the meterstick through the clamp until the stick is balanced on the stand.  The balancing point is called the center of mass of the meter stick.  Record this point.

- Case 1.  With the meter stick on the support stand, suspend a mass  at the 15-cm mark on the meterstick.  Then adjust the lever arm for a mass  at the other end of the meterstick.

- Record the masses and position x as read on the meter stick and then record the lever arms.  Compute the torques and find a percent difference between the clockwise ((cw) torques and counterclockwise ((cc) torques.

- Case 2.  Place  at the 20-cm mark and  at the 60-cm mark on the meter stick.  Experimentally determine the position for  so that the system is in equilibrium. Follow a procedure similar to steps 2 and 3.  Compute the percent difference between the clockwise and counterclockwise torques.

- Case 3.  Place an unknown mass at the 10 cm mark of the meterstick.  Suspend from the other side a counter mass  and adjust its position until the system is in static equilibrium.   Using, , calculate the unknown mass m1.  Remove the unknown mass and determine its mass on the laboratory balance.  This is the accepted mass. Calculate % error.

- Case 4.  Suspend a mass  at or near the zero end of the meterstick.  Move the meterstick in the support clamp until the meterstick is in equilibrium. Record this new equilibrium position as xo’. Using the total mass of the meterstick, calculate the clockwise and counterclockwise torques, and then calculate a percent difference.  In this calculation, you will include the mass of the meter stick as if it were concentrated at its center of mass, xo (around the 50 cm mark) calculating the lever arm to the new pivot point.

Data Table

Mass of meterstick, mmeterstick ______________________

Balancing point (center of mass) of meter stick, x0 = ______________

* Attach a sheet to the laboratory report showing diagram and calculations for each use.

| Values | Moment (lever) arms | Results *(see note above) |
| --- | --- | --- |
| Case 1 |
| m1 = 100 g x1 = 15 cm m2 = 200 g x2 =_________ | r1 = ___________ r2 = ___________ | (cc = ___________ (cw = ___________ Perc.Diff. __________ |
| Case 2 |
| m1 = 100 g x1 = 20 cm m2 = 200 g x2 = 60 cm m3 = 50 g x3 = _______ | r1 = ___________ r2 = ___________ r3 = ___________ | (cc = ___________ (cw = ___________ Perc.Diff. __________ |
| Case 3 |
| m1 =? x1 = 10 cm m2 = 200 g x2 =_________ | r1 = ___________ r2 = ___________ | m1 ____________ (measured on scale/ accepted) m1 ____________ (calculated, experimental) Perc. error _________ |
| Case 4 |
| m1 = 100 g x1 = ________ mmeterstick = _______ xo = _______ xo’ = _______ | r1 = ___________ r2 = ___________ | (cc = ___________ (cw = ___________ Perc.Diff. __________ |