Name: _____________________________

## Specific Heat

#### Equipment Needed

Density cubes, large with hooks   F2-L

Clamp, Pendulum G3-L

Styrofoam cups for calorimeter   BB5-L

Extra cup for water storage   BB5-L

Cup, for boiling   FF2-L

Hot plate   FF2-L

60cm ½” dia rod   L5-L

Scale, Digital DD4-PR

String with paper clip   DD8-PR   (in back)

Thermometer, Digital   Y6-PR

Paper towels   Y4.5-L

### Objective

The purpose of this lab is to determine the specific heats of several different metals.

#### Introduction

If you mix hot and cold water together, the temperature of the final mixture depends on how much hot water is added to how much cold water.  If you throw a hot branding iron into a pail of cool water, you know that the temperature of the iron will go down.  You also know that the temperature of the water will rise--but will its rise in temperature be more, less, or the same as the temperature drop of the iron?  That is, will the temperature of the water rise as much as the temperature of the iron goes down?  Or will the changes of temperature instead depend on the relative masses of the iron and the water?

In this experiment, you are going to investigate the quantity of heat per gram per degree (Celsius), known as the specific heat.  Water has a specific heat of 1.00 cal/gC--relatively large compared to most substances.

The heat (Q) lost by a specimen, say a piece of metal, submerged in water equals the heat (Q) gained by the water and by the container.  In this experiment we will neglect the heat absorbed by the Styrofoam container, as it is negligible.

Qlost = Qgained Heat, Q = Specific Heat of Substance x Mass of Substance x Change in Temperature. Heat lost by metal block = Heat gained by water CmMm(Tim - Tf) = CwMw(Tf - Tiw) Equation 1

Where Cm   =  specific heat of the metal

Mm  =  mass of metal

Tim    =  initial temperature of the metal

Tf     =  final temperature of metal and water

Cw   =  specific heat of water

Mw  =  mass of water

Tiw   =  initial temperature of water

Fig 1A basic setup  					Fig 1B attachment point for mounting rod

Fig 2A   calorimeter cup (styrofoam cup)    with lid 			Fig 2B  sample in cup 	     Fig 2C  cup w/sample + lid

+ thermometer

### Procedure          Prevent electrical cords, string, Styrofoam cups, etc, from coming in

### contact with the hot plate!

- Begin by boiling water in the provide metal cup. The cup should be filled with enough water to cover the sample.

- Find the mass of the metal  (Mm) and record it in the table.

- Attach a piece of string to the metal and lower it into the beaker.  Be sure the metal is completely. immersed in the water.  Heat the metal in the water for at least 5 minutes.  Our assumption will be that the metal’s temperature is the same as that of the boiling water.  Measure and record the temperature of the boiling water.  This is equal to the initial temperature of the metal (Tim)

- Find and record the mass of the empty calorimeter cup. (Mc).

- Fill the calorimeter cup about one-half full of cold water (about 3 below room temperature) and find the mass of the cup and water  (Mcw).
Subtract the mass of the cup to obtain the mass of the water in the cup (Mw).

- Find and record the initial temperature of the water (Tw).

- Holding the metal block by the string, quickly (but carefully) transfer the metal block into the calorimeter cup.

- Stir and record the temperature of the water when it reaches its highest point (Tf).

- Calculate the specific heat of the metal by using Equation 1.

- Compare the specific heat of the metal by its accepted value.  Calculate the percent error.

- Repeat the above procedure for a different metal.

Data Table

| Type of Metal | Mass of Metal Mm (g) | Mass of cup + water Mcw (g) | Mass of cup Mc (g) | Mass of Water Mw (g) | Tim oC | Tiw oC | Tf oC | Spec.Ht. Experi. (cal/goC) | % error |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Specific Heats for Laboratory Samples at 20o C |
| --- |
| Fe 0.119 | Cu 0.092 | Sn 0.054 | Zn .0925 | Al 0.214 | Pb 0.0306 | Brass .0917 |